# Specific settings for KI runs

## Run0

##### EXTENT:
MIDDLE : -35.84, 137.00
want left to right > 0.94 degrees (and must be less than 2 degrees to avoid missing SRTM area)
want bottom to top > .4 degrees (and must be less than 1.68 degrees)
338 < npts_x < 714 (at .0028)
143 < npts_y < 600 (at .0028)
npts needs to be nprocs * 24
14 < nprocs_x < 29
5 < nprocs_y < 25
Procs inner product needs to be divisible by 48:
nprocs_y, nprocs_x = 10,24 (240 = 48*5)
grid points need to be nprocs * 24:
npts_y, npts_x = 240, 576

##### Fire inputs
For fire ignition polygon and fuel load/fire settings see fire.inp on GADI at /home/574/jwg574/cylc-run/au-aa929/app/um/file/fire.inp
Constant fuel, single large polygon ignition, DF = 12.5, …